## Slide 1: <Host> mbed Hello World
<Location>
<Date>
Notes: Revision History
0.1 Published to http://mbed.org/cookbook/Workshop
<number>

## Slide 2: Agenda
ARM Overview
  What does ARM do?
<Host> Overview
  What does <Host> do?
mbed
  Introduction to mbed
  Lab 1 mbed registration and hello world demo
  Lab 2 Rapid prototyping: Creating a file system
Lunch and discussion

## Slide 3: What does ARM do?
ARM designs technology that lies at the heart of advanced digital products
Notes: General overview of the type of products and markets ARM technology goes into

## Slide 4: ARM Overview
ARM is the world’s leading semiconductor IP company and The Architecture for the Digital World ®
Over 15 billion ARM technology based chips shipped to date
Unrivalled Partner ecosystem
  Over 640 processor licenses sold to more than 200 companies
  Millions of developers; billions of users
ARM has the right technology – optimized for a mobilizing world
We’re customer-focused – listening harder and responding faster

## Slide 5: Rapid Prototyping for Microcontrollers
Notes: <number>

## Slide 6: What’s happening in Microcontrollers?
Microcontrollers are getting cheap
  32-bit ARM Cortex-M3 Microcontrollers @ $1
Microcontrollers are getting powerful
  Lots of processing, memory, I/O in one package
Microcontrollers are getting interactive
  Internet connectivity, new sensors and actuators
Creates new opportunities for microcontrollers
Notes: What’s Happening In Microcontrollers
Microcontrollers are now getting very cheap. A Cortex M3 MCU can now be bought for around $1, compared to $10 in the not so distant past. This rapid reduction in price looks set to continue with Cortex-M0 MCUs announced.
Compared with previous generations of microcontrollers that performed in the tens of MHz, and with modest Flash/SRAM (32kB/8kB), Cortex-M3 MCUs are available with 512kB Flash and 64kB SRAM, clocking at 100MHz and higher. They also contain a rich feature set of interfaces, USB, Ethernet, SPI, I2C, I2S, UART, CAN, PWM, Analogue in and out, and of course lots of GPIO.
With the Ethernet and USB interfaces comes interactivity, this can be either with a host computer or with the internet directly, pushing and pulling data and communicating. Sensor/peripheral technology is keeping pace with things like RFID readers, touch screen LCD, MEMS devices such as gyros, capacitive, pressure and force sensing (and much more). The newer generation of peripherals are accessible and affordable for new product designs, and conceptually very easy to connect to an MCU based system, using standard interfaces such as UART, SPI and I2C.

## Slide 7: Opportunities for Microcontrollers
Before 1980 computers were used and applied by computer scientists
now they are:
  Applied across all industries
  Widely used in the home
  Used by almost anybody
Currently microcontroller technology is mainly applied by the embedded professional
Microcontrollers interact with “the real world”
  Sensors, actuators and communication, define their application
  Their potential is greater than the home computer
Notes: Applying Microcontroller Technology
Before the computer revolution of the 1980s computers were only understood, used and applied by scientists. 25+ years after the revolution, computers are everywhere, applied in all industries, widespread in the home, accessible and applicable by almost anyone.
Computers were the solutions looking for problems to be applied to. The computer scientists did not produce all the applications, they enabled people with insight to apply them to their own problems. The number of people able to apply computers to their own problems is orders of magnitude greater than the number of computer scientists.
Microcontrollers are solutions looking for problems. Traditionally, the people applying them are the embedded engineers who have trained to be able to develop hardware and software, and understand how to get the very best from the hardware, software and tools. However, people who see the problems and appreciate that a microcontroller can solve are not only the to be embedded engineers.
New products concepts are defined by interactivity and communications, and increasingly come from product designers whose expertise is not in embedded engineering. However, they can see the problem that needs to be solved, and understand how they might do so by applying microcontroller technology.
Microcontrollers interact with the real world through sensor, actuator and communication technology, and they often do so invisibly without even being noticed. Their scope of application is potentially far greater than that of the home computer.
Do not underestimate the potential for micrcocontrollers.

## Slide 8: Barriers for Microcontrollers
What prevents microcontrollers from being designed in?
Conceptually simple things can be hard to prototype
  I want to send an SMS when my plants need watering
Repetition of choices to make:
  Microcontroller
  Tool chain
  Dev board
  Sensors
  It’s not difficult, but can be tedious and time consuming
Overhead for starting a new project
  Fine for a long complex projects
  A deterrent for quick experiments and tests
Notes: Microcontrollers almost have their own built in barriers.
It is easy to identify a problem, and conceive a solution that might be implemented with Microcontroller technology, but the reality is that it is difficult to experiment and prototype quickly and easily.
When starting a new project, it is common to have to make a number of choices. They may not be complex, but they are time consuming, tedious and may feel unnecessary if the project happens to be a quick experiment. However, they still have to be made. Someone new to microcontrollers might not understand the choices that they have to make, they may be overwhelmed with options which for the scope of their experiment may not even be relevent.
Finally, there is often a certain amount of overhead in starting a new project. Setting up the work space, configuring the hardware, wiggler, tools. This is fine for longer term project, but for quick experiments, the overhead may be the most time consuming part!

## Slide 9: Rapid Prototyping
3D Moulding
3D Printing
2D/3D Design
Web Frameworks
Rapid Prototyping helps industries create new products
  Control, communication and interaction increasingly define products
  Development cycles for microelectronics have not kept pace
Notes: Other industries have Rapid Prototyping solutions, as it is clear that the best way to stimulate new designs is to enable prototyping fast and often.
With 3D moulding and printing – You can move from a CAD model of an object, into a high quality prototype using these techniques, the machines not being much bigger than an office photocopier.
Schools, colleges and Universities have this sort of equipment. You can readily submit your CAD model for 3D printing at various Online 3D printing houses, pay modest fee by credit card and receive the result a couple of days later by post.
2D/3D Design. You can very easily design artwork, interactive animations, and prototype user interfaces using various PC applications. These are the sort of applications that are readily available and accessible for the home user
Web frameworks. For new web applications, a whole host of frameworks exist. They are configurable, well supported by their communities, and extendible with plug ins. It is now very fast to build web based prototypes with very little invested time or effort.
Electronics and Software. The final link in the chain for a product prototype may well be to put a PCB in the plastic case it took you 2 hours to design and mould. You have to capture the design schematically, lay it out on a PCB, send it for manufacture (3 days considered fast), Find an assembly house that will build small batches (at a premium), or hand solder your self (not for the feint hearted). When it is assembled and tested, you can start writing software. Time elapsed, probably a week or more.

## Slide 10: mbed.org - Rapid Prototyping for MCUs
Fastest way to get started with ARM microcontrollers
  Plug ‘n’ Play Hardware, Online Compiler
  Get setup and run “Hello World!” in 60 seconds
  Removes entry barriers to MCU technology
Focused on rapid prototyping for a diverse audience
  DIP form-factor, High-level APIs, Developer website
  Technology and tradeoffs to enable fast experiments
  Creates new applications for MCU technology
Launched at ESC Boston with live demo
  Internet-enabled “Twittering Billy” read out tweets
  An embedded internet device, prototyped in ½ day
  Over ¼ million video views in first week!
Notes: Nothing really to add to the slide text

## Slide 11: mbed Approach
Focus on tools supporting the earliest stage of design
  Point of entry and Getting Started
  Experimentation and Rapid Prototyping
Apply technology and trade-offs that support this goal
What mbed is not trying to do:
  Replace Keil MDK or other professional tools
  Replace development or evaluation boards
Proof of Concept
Specification
Implementation

## Slide 12: mbed Rapid Prototyping Platform
Complete Hardware, Software and Web 2.0 Solution
Lightweight Online Compiler
Prototyping Form-Factor
Dedicated Developer Website
High-level Peripheral APIs
Notes: The main thing here is to play down the actual microcontroller. It might be the only thing you can hold in your hand but is less and 25% of the value of mbed
1. Dedicated developer website. Information, resources, manuals, forum, mechanisms to share code among users. This website is exists solely to make it easier to experiment with microcontrollers
2. Lightweight online compiler. Includes an industry standard RVCT4.0 back end, but has a simply GUI, with all options defaulted to suit the common case. We made some tradeoffs, because we know best. When you need the extra flexibility, you then know best, and it is probably time for you to move to a traditional development flow. By now you have proved your concept with mbed, and are now developing a product with traditional tools.
3. Peripheral APIs and libraries. The microcontroller has a library that abstracts the peripheral to an API that relates to what you might want to do with it. For SPI, you want to send bytes and receive bytes. You don’t care how it happens at this stage, it is just a prototype
4. The microcontroller has a 0.1” DIP form factor suitable for prototyping. It powers from USB and has a drag and drop programming interface, as well as a Serial interface available over USB too. Great for getting going fast

## Slide 13: mbed Website
Dedicated Developer Web Platform
  Custom Web 2.0 tools and environment focused on developers
  Simple route to get started, comprehensive resources and support
http://mbed.org
Notes: Handbook – A reference for the interfaces, the API, the board specification. All the hard facts you need to get going.
Forum – For sharing ideas, discussing, networking
Cookbook –For publishing projects and code
Blog – To keep updated with what is happening in the world of mbed.

## Slide 14: mbed Compiler
Lightweight Online Compiler
  Web 2.0 browser-based IDE with personal workspace “in the cloud”
  Nothing to install or configure, login from anywhere
  Industry leading RVCT 4.1 back end. It is a real tool
Notes: The important thing to stress here is the zero install, and that the compiler and projects are in the cloud
It’s like web mail, Pick up where you left off, hop from computer to computer.
The back end is RVCT 4.0, so it is really just web access to a high end compiler that has it’s flags and options defaulted.
It is also a full license, not an evaluation licences. It doesn’t expire, it isn’t limited in any other way than targeting the mbed hardware

## Slide 15: mbed Library
High-level Peripheral APIs
  Trading memory and CPU performance for ease of use
  Abstract software interfaces for controlling microcontroller hardware
  Intuitive peripheral access, encapsulation of implementation details
  Treat hardware and software the same
Notes: This slide is to show that the representation of an interface is the same in software as it is in hardware. It keeps a very clean simple view on how to control things.
The pin out cards makes it obvious, for instance, where the SPI blocks are and how you wire them.
In software, it is the same scheme - it is a SPI object declared with the pins specified.
You can swap the pins in the software, swap the declaration, and your code will work relocated to the new location.

## Slide 16: mbed Microcontroller
Cortex-M3 MCU in a Prototyping Form-Factor
  0.1” pitch DIP with “USB Disk” interface and support components
  Nothing to install or configure, practical for breadboard and PCBs
Notes: The important headlines are :
0.1” pitch, ideal for breadboard, and stripboard
Powered over USB
USB flash disk for programming
debug via LEDs and Serial over USB
You can access the USB file system from your code, a great feature for data logging or runtime configuration

## Slide 17
Lab 1
mbed registration and hello world
Notes: Here is where we do a live demo.
Plug in mbed
Go to the website,
Getting Started
Downloading A program
Compiling a Program
Take the tour
Handbook
Cookbook
Forum
Blog

## Slide 18: Registration
mbed microcontroller enumerates as a Mass Storage Device (USB disk)
double-click the mbed.htm file on the mbed USB disk
Log in or sign up for a new account
The mbed microcontroller contains your license to the compiler
Notes: When you connect the mbed board, it presents itself as a standard USB Flash disk which the operating system can communicate with. This means that it can be plugged into a PC, Mac or Linux machine with no additional drivers.
The flash disk contains an HTML file that, when clicked, will open a web browser and direct you to http://mbed.org, where you can sign up for an account, or log in if you already have one.
The mbed Microcontroller contains a license that can be used to create exactly one mbed user account.

## Slide 19: Getting Started
Useful resources linked from the first page, including very clear links to “Hello World” and the Getting Started guide
Compiler linked from front page
Notes: On the front page of the mbed website are some useful resources. These are aimed at getting the new user up to speed as quickly as possible.
The first of these is a pre-built binary which can be saved to the mbed Microcontroller and run. It is a simple LED blinking program that proves that the binary is being downloaded and run correctly.
Next is the getting started guide. This is a walkthrough tour leading all the way through to compiling and running your first simple program.
It should be possible for a new user to have run through all these steps in a just a few minutes.

## Slide 20: Getting started
Create or open a project in the Program Workspace
Develop code in the text editor
Save and compile
Compiler outputs
  Errors and warnings
  -or-
  A downloadable binary
Save to the USB flash disk
Notes: The online compiler is a very simple IDE with RVCT installed on the web server back end. All of the options have been preset and are not configurable.
All the files are stored on the server, and all the editing is done locally, so the only internet traffic is when loading or saving files, or downloading a completed binary.
Being a regular compiler its output is what you’d expect. Errors and warnings with line numbers, and hints as to how your code is wrong, or a completed binary, ready to be saved to your mbed Microcontroller.

## Slide 21: Getting started
Once the file has saved to the flash disk, it needs to be programmed into the microcontroller
Press the button on the mbed module
Your code will start running!
Notes: It is important to understand that the USB interface is a separate entity to the microcontroller running the binary.
When you save a binary to the mbed flash drive, you have done just that, stored a file on a flash drive. When you press the reset button on the mbed, the last binary file to have been saved onto the flash drive will be loaded into the microcontrollers memory, and run.
You can store other types of file on the USB flash disk, they will be ignored. Keep in mind that the flash drive has just 2Mb capacity.

## Slide 22
Lab 2
Rapid Prototyping: Data Logging

## Slide 23: Example : Data Logging
Applications often include data logging capabilities, and access to the data often involves bespoke software and interface cables.
This example shows how standard methods and interfaces can be used to display, save and retrieve data from an application
For the purposes of the experiment, we will be displaying and logging noise from an unconnected ADC
  Touching the pin will influence the noise
  It is a demonstration, imagine it is real data!
Notes: The USB flash drive which you save your binary files to is accessible from your program, using standard C functions fopen, fread, fwrite, fseek, fclose. When your program is using the flash disk, it will temporarily disappear from the PC, and will return when the files are closed.
This has proven to be a very useful feature for prototyping features such as run time configuration of a program, reading command files and of course data logging application. The base class “FileSystem” can be derived to work on any storage which can be exposed as block read/write. An SDCard class already exists, and other variants such as discrete SPI flash are easily possible.

## Slide 24: Example : See the data
The USB connection to mbed can also be used to provide a serial port
Windows requires a driver, linux and Mac “just work”
http://mbed.org/handbook/SerialPC
Standard C functions, printf and scanf
This example displays 100 samples to a terminal application
Notes: The USB flash drive which you save your binary files to is accessible from your program, using standard C functions fopen, fread, fwrite, fseek, fclose. When your program is using the flash disk, it will temporarily disappear from the PC, and will return when the files are closed.
This has proven to be a very useful feature for prototyping features such as run time configuration of a program, reading command files and of course data logging application. The base class “FileSystem” can be derived to work on any storage which can be exposed as block read/write. An SDCard class already exists, and other variants such as discrete SPI flash are easily possible.

## Slide 25: Example : Data Logging
The mbed Flash disk is accessible from user code using the LocalFileSystem object
Standard C file handling techniques apply
fscanf for runtime configuration
fprintf for data logging purposes
This example logs 100 samples to a CSV file
Notes: The USB flash drive which you save your binary files to is accessible from your program, using standard C functions fopen, fread, fwrite, fseek, fclose. When your program is using the flash disk, it will temporarily disappear from the PC, and will return when the files are closed.
This has proven to be a very useful feature for prototyping features such as run time configuration of a program, reading command files and of course data logging application. The base class “FileSystem” can be derived to work on any storage which can be exposed as block read/write. An SDCard class already exists, and other variants such as discrete SPI flash are easily possible.

## Slide 26: Data quickly visible to a PC
Logging to a CSV file means Excel can open the file and interpret, manipulate or plot the data.
While the program executes the flash drive disappears from the PC, and returns when the file is closed

## Slide 27: Extend it to store lots of data
GND
MISO – p6
SCL - p7
Vcc
MOSI – p5
nCS - p8
Perhaps a final system might want to store lots of data
  SD cards are ideal, ubiquitous and recognisable by everyone
Hardware for an SD Card is minimal
  SPI Port connection using simple breakout
As before, mbed keeps it simple

## Slide 28: Extend it to store lots of data
Import the SDFileSystem Library into the project
Include the SDFileSystem header
Swap LocalFileSystem for SDFileSystem
Everything else remains the same
Notes: The USB flash drive which you save your binary files to is accessible from your program, using standard C functions fopen, fread, fwrite, fseek, fclose. When your program is using the flash disk, it will temporarily disappear from the PC, and will return when the files are closed.
This has proven to be a very useful feature for prototyping features such as run time configuration of a program, reading command files and of course data logging application. The base class “FileSystem” can be derived to work on any storage which can be exposed as block read/write. An SDCard class already exists, and other variants such as discrete SPI flash are easily possible.

## Slide 29: What about a USB drive?
USB Host hardware is minimal; a USB A connector
VCC -> VU
D- -> D-
D+ -> D+
GND -> GND

## Slide 30: What about a USB drive?
On your project, right click -> Import the files for MSCFileSystem
      http://mbed.org/users/chris/programs/MSCUsbHost/5z8fm
    Add #include for MSCFileSystem
    Call it “fs”, as before
    The change in storage medium is transparent to the application
Notes: The important point here is similar to when we introduced the LocalFileSystem, that there are very few changes.
<number>

## Slide 31: Summary
There is huge opportunity for microcontroller applications
  A major barrier to adoption is simple experimentation
mbed helps with getting started and rapid prototyping
  Fast turnaround of experiments and prototyping new ideas
  Try out new technology and new ideas
Makes the technology very accessible
  Demo showed a start to finish prototyping example
  From getting a user started to enabling an application experiment
Use at as a tool when you need to experiment!

## Slide 32: Summary
A solution focused on prototyping has a broad appeal
Engineers new to embedded applications
  Enables experimentation and testing product ideas for the first time
  Create designs where electronics and MCUs are not the focus
Experienced engineers
  Provides a way to be more productive in the proof-of-concept stages
  Introduce 32 bit microcontroller technology to existing designs
Marketing, distributors and application engineers
  Provides a consistent platform for demonstration, evaluation, support
  Make promotion of MCUs more effective and efficient

## Slide 33
Q&A