## Slide 1: MBED Coffee Roaster
Eric Patterson
Elza Mathew
Erin Deye

## Slide 2: Project Description
For our design project we created a temperature controlled coffee roaster. We used a nichrome wire to roast the coffee beans and an AC motor to rotate the basket holding the beans so that they were roasted evenly. A thermocouple read in the internal temperature, and a hysteresis controller was used to regulate the heating element. The user is able to control the temperature of the system using a touch panel. They are also able to monitor the temperature and elapsed time on an LCD screen.

## Slide 3: Components List & Initial Sketch
Mbed (LPC-1768)
K-Type Thermocouple (MAX31855)
LCD Screen (uLCD-144-G2)
Capacitive Touch Panel (MPR121)
Solid State Relay (SSR-40DA)
Nichrome Wire (19-AWG, 14.5A, 190”)
High Torque Low Speed AC Motor
Misc. Materials:
  Basket to hold coffee beans
  Ceramic supports for nichrome wire
  Box to hold roasting system

## Slide 4: Control System Block Diagram
mbed
LCD Screen
Capacitive
Touch Panel
Thermocouple
Solid State
Relay #1
Solid State
Relay #2
Vin
GND
D0
CS
CLK
Gnd
SDA
SCL
IRQ
Vcc
5V
GND
TX
RX
RES
P3
P4
P3
P4
Vout
GND
P10
P9
P11
GND
P28
P27
P26
Vout
Vout
GND
P6
P20
P7
P22
GND
P30
GND

## Slide 5: Heating System Block Diagram
Solid State
Relay #1
Solid State
Relay #2
Motor
Wall Outlet
Nichrome Wire
P1
P2
P1
P2

## Slide 6: Control System

## Slide 7: Heating System

## Slide 8: User Interface
Motor
On
Motor
Off
Reset Temp.

## Slide 9: Coffee Bean Roaster Protocol
Procedure:
Power control system.
Set temp. to 450 degrees.
Turn on motor.
Set temp. reached.
Put in beans.
Follow heating profile.
Pour beans out.
Turn off entire system.

## Slide 10: Working Coffee Bean Roaster
https://www.youtube.com/watch?v=uuBk4l6XnQU

## Slide 11: Coffee Beans Before and After

## Slide 12: Results
Preheats to 450 F degrees in approx. 20 minutes.
Accuracy: -1 degree to +3 degrees from set temperature.
Up to 1 lb. of beans can be roasted at a time.
Roasting takes approx. 12 minutes.

## Slide 13: Future Work
“Internet of Things” - twitter, website, or app
Improve bean load and unload
Heating element – make faster, bigger heating element, currently takes some time to get up to temperature.
Better user interface – larger screen.
Wire management.
Plot graph of temperature over time.

## Slide 14: Notebook Page
http://developer.mbed.org/users/ericspatterson/notebook/mbed-coffee-roaster/