## Slide 1: Hands-On Workshop: ARM mbed™
FTF-DES-F1302
JUN.2015
Sam Grove - ARM
Michael Norman – Freescale

## Slide 2: Agenda
What is mbed
mbed Hardware
mbed Software
mbed Tools
mbed Support and Community
Hands-On Workshop – FRDM-K64F

## Slide 3: What is mbed

## Slide 4
Things
Internet
mbed™ is about creating the Things
Cloud Services and Platforms

## Slide 5
Assembler
C
Platform
1990s
2000s
2010s

## Slide 6
mbed.org
Partners
{ silicon }
{ ecosystem }
{ cloud }
Developers
{ 125k people }
Software
{ sdk }
{ 12k repos }
Hardware
{ 63 platforms }
Components
{ 332 components }
Offline Tools
{ 10 Options }

## Slide 7: mbed Hardware

## Slide 8: Freescale Freedom Boards
Kinetis K Series
FRDM-K20D50M for Kinetis K20 MCUs
FRDM-K22F for Kinetis K22 MCUs
FRDM-K64F for Kinetis K64, K63, and K24 MCUs
Kinetis L Series
FRDM-KL02Z for Kinetis KL02 MCUs
FRDM-KL03Z for Kinetis KL03 MCUs
FRDM-KL05Z for Kinetis KL05Z and KL04Z MCUs
FRDM-KL25Z for Kinetis KL1x and KL2x MCUs
FRDM-KL26Z for Kinetis KL16 and KL26 MCUs
FRDM-KL46Z for Kinetis KL3x and KL4x MCUs

## Slide 10: OpenSDA & DAPLink Interface Firmware
Target Processor
nRESET
UART RX/TX
SWD / JTAG
MSC Bootloader
Debug MCU
K20DX128Vxx5
DAPLink
Interface
Firmware
OpenSDA Hardware Circuit
SPI, GPIO
UART TX/RX
USB
Composite
Device
Computer
IDE
File System
Serial Terminal
GPIO / ADC
LED
GPIO
PWM
DAPLink Interface Firmware includes:
  USB HID CMSIS-DAP Run-control debug interface
  USB MSC disk for drag ‘n’ drop flash programming
  USB CDC serial interface between the host and target

## Slide 11: FRDM-K64F Overview
Quick, simple development experience with rich features
  Easy access to MCU I/O
  3-axis accelerometer/3-axis magnetometer
  RGB LED
  Add-on Bluetooth Module
  Built-in Ethernet/Add-on Wireless Module
  Micro SD
Arduino shield compatible
Flash programming functionality
enabled by OpenSDA debug interface
$29.00

## Slide 12: Arduino Shields

## Slide 15: mbed Software

## Slide 16: mbed SDK Software Stack
Networking and USB stacks
CMSIS-RTOS implementation
Easy-to-use C++ APIs
stdlib setup, board support, systems configuration
Hardware Abstraction Layer (HAL) for MCU peripherals
CMSIS-CORE: hardware register access and Cortex-M startup code
mbed common
C/C++ User Application
mbed API
mbed HAL Implementation
SDK Adapters
CMSIS-CORE
Components
Middleware
Networking
MCU Registers

## Slide 17: mbed Program Example
Hello World example
  All startup code is taken care of by the mbed SDK – user code starts at main()
  Definition of a digital output variable, myled
  Use of overloaded “=“ operator
  Alter digital output (and LED) by simply assigning a value to the variable.

## Slide 18: http://developer.mbed.org/ handbook

## Slide 19: Digital Inputs and Outputs

## Slide 20: Ticker

## Slide 21: http://developer.mbed.org/ components

## Slide 22: Component Database
Components are portable across all platforms and tools

## Slide 23: Component Entry
Example program to evaluate the component
Directly import into
Your current program

## Slide 24: FXOS8700Q

## Slide 25: http://developer.mbed.org/cookbook

## Slide 26: mbed Tools

## Slide 27: mbed Online IDE
Cloud-based ARM professional C/C++ compiler
  Private account based access
  Pre-configured compiler that “just works”
  Informative compile-time messages with links to error and error message wiki
  Provides build information including RAM and flash usage is a graphical display
  Generates binary: save to mbed enabled hardware
Browser-based editor and project manager
  Syntax highlighting
  Keyboard shortcuts
  Integrated project manager
  Tabbed file organizer
  Code auto-formatter
Easily imports mbed software
libraries and examples
Runs on Windows, Mac iOS,
Android, Linux

## Slide 28: Online IDE and Compiler
Integrated Version Control
Programs Workspace
Program/Library Details
Platform Selection

## Slide 29: Revision Control and Collaboration
  Built-in revision system
  Mercurial DVCS
  Collaboration workflow
Local version control
  Commit a version of your project, and view the revision history
  View changes a version made, and compare changes between versions
  Switch and revert to a different version
  Branch and merge versions
Collaborate with others
  Pull - Copy changes from remote repository to a local repository in your workspace.
  Push - Copy changes from local repository to a remote one.
  Fork - Create remote repository on mbed.org from imported local repository
  Publish - Publish changes to existing repository (push) or create new one (fork)
  Update - Pull from a remote repository and switch your local repository to the latest revision.

## Slide 30: Exporting to Offline Tools
The mbed Compiler can export to professional toolchains:
  Kinetis Design Studio
  Keil uVision
  ARM DS-5
  GCC
  IAR Embedded Workbench
  CooCox
  Emblocks
  Zip with repositories
Why export?
  Run-control debug
  Optimizations
  Automated testing

## Slide 31: mbed Support

## Slide 32: mbed Community
Cloud services
Vendors
Manufacturers
Components
Operators
Developers

## Slide 33: mbed Community Support
Worldwide community of developers
Shared context of
  common tools
  common SDK
  common hardware
  common experiences
Issues can be reproduced and resolved efficiently

## Slide 34: mbed – Moving from Prototype to Production

## Slide 35: Open Source Software
mbed SDK was open sourced in Feb, 2013
Full source code now available
Apache 2.0 Open Source License
  Can modify the source
  Can distribute
  Can sublicense
  Allows use in commercial products
  Not required to open-source the resulting software

## Slide 36: Open Source Software
Import it into the online IDE:
Clone the GitHub repository:

## Slide 37: mbed Test Tools and Build Scripts
mbed sources include Python build and test scripts
Released under Apache 2.0 license
Build system
  command line builds of libraries
  build and run test projects
Test system
  automated test scripts
  Scripts can program and reset the target
  Results are printed over serial port
pyOCD: python library for accessing CMSIS-DAP

## Slide 38: Script commands
> python build.py –m K64F –t GCC_ARM –j0 -c
> python project.py –m K64F –i kds –c –p 25

## Slide 39: Hands-On

## Slide 40: Hands-On Agenda
Lab 1 – Hello World
    Input / Output and serial module
    Challenge – Change LED state based on button state
    Challenge – Read serial characters and change RGB LED state
Lab 2 – Interrupts and Timers
    Interrupts and timers
    Challenge – Drive RGB LED while sleeping between state change
    Challenge – Change RGB LED state but sleep between state change
Lab 3 – Using Sensors
    I2C accelerometer / magnetometer
    Challenge – Control an LED in a meaningful way based on the sensor readings
    Challenge – Add sensor handling using the RTOS
  h t t p : / / m b e d . o r g / f t f 2 0 1 5

## Slide 41: Creating an Account
  Connect a mbed platform to a Windows / Mac / Linux computer
Registration
  mbed platforms is identified as a mass storage device (USB disk)
  Double-click the mbed.htm file on the mbed USB disk
  Log in or sign up for a new account

## Slide 42: Know your Hardware
Connection diagram and example programs on the platform page
Connection
Diagram
Example
Program

## Slide 43: About Programs

## Slide 44: Compiling your Program